## Slide 1: Building Your Go-Kit
Robert Anglin, WX5TEX

## Slide 2: The Process
Components
Layout Process
Determine Your Need
Form Factors

## Slide 3: Determining Your Needs
Your kit will vary depending on the event, season, location
Ideally, you may have multiple kits
Once your kit is built, USE IT & modify it
Deployment Types
Public events & drills
Field day, camping, SOTA, NPOTA
Emergency Deployments

## Slide 4: Form Factors
The humble bag
The rugged ammo can
The organized rack case
The resilient storm case
The elite custom enclosure

## Slide 5: The Layout Process

## Slide 6: Critical Components
Radio
Power
Antenna
Digital Components
Power Management
Power Components:
AC power supply
12v battery
PwrGate
Rig Runner (distribution)
Voltage monitoring
Solar charge controller

## Slide 7: Battery Options
Option 1
1x 55ah SLA battery
Option 2
2x 35ah SLA batteries
Option 3
5x 10ah LiPo batteries
Option 4
2x 20ah LiFePo4 batteries
$100
50 lbs
$110
45lbs
Ability to charge one while running on other
$400
14 lbs
$250
12lbs
Requires special charging equipment
Longest shelf life and life cycle
Recommended goal: 55ah of power

## Slide 8: Auxiliary Components
Lighting
Cooling
Auxiliary charging
Storage for other parts such as microphones, coax
Logbook

## Slide 9: Hints & Kinks
Approach your build like a game of chess. Always think 10 steps ahead
Measure equipment by hand, don’t rely on manufacturers published specs
ARRL’s Hints and Kinks book
High speed, low drag
Deb’s NASA-certified herculean Velcro
Silicon adhesive
Warranty “void if removed” stickers are no longer legal