## Slide 1: Multnomah County ARES
Introduction to HSMM and Mesh Networking
Brian Cochrane, KE7QPV KE7QPV@arrl.net

## Slide 2: What is HSMM?
High Speed Multimedia – digital transmission of data/images/audio/video over Amateur Radio microwave frequencies
Data rates of 1Mbps to 130Mbps – hundreds to thousands of times faster than Packet Radio
WiFi equipment, operated under FCC Part 97 rules instead of Part 15

## Slide 3: FCC Part 15 vs. Part 97
Part 15: Unlicensed, Consumer WiFi
Part 97: Amateur Radio, HSMM
Unlicensed; must not interfere with licensed users
900MHz, 2.4GHz, and 5.8GHz bands
Max TX power 1W; lower with antenna gain >6dBi
Licensed as primary or secondary user
900MHz, 2.4GHz, 3.4GHz, and 5.8GHz bands; some non-Part 15 frequencies
Max TX power 1.5kW; no antenna gain restrictions

## Slide 4: What can we do with it?
Video
Voice
E-mail; instant messaging
File transfers; web services
Just about any other application that can run on a TCP/IP network

## Slide 5: Examples of HSMM uses for Emcom
Backup Internet link for EOC
Data/voice link between shelters and operations/logistics
Remote video feeds for situational awareness

## Slide 6: Distance
Dependent on many factors – TX power, RX sensitivity, antenna gain, noise, obstructions
Ubiquiti claims 30km+ for some devices
HamWAN Puget Sound Data Ring has several links in the 30~60 mile range

## Slide 7: Technical Limitations
Clear line of sight required (900MHz can handle some foliage and other obstructions) - antennas need to be above buildings and trees
Microwave frequencies are attenuated by moisture - fog and heavy rain can affect link
High noise floor on 900MHz and 2.4GHz due to WiFi equipment, cordless phones, and other Part 15 devices

## Slide 8: Network Topology
Point to Point (PtP) – single link between two radios
Point to Multipoint (PtMP) - links between two or more radios and one common radio; also called Star or Hub and Spoke topology
Mesh - each radio has multiple links to other radios
Hybrid – some combination of PtP, PtMP, and/or Mesh

## Slide 9: Point to Point (PtP) Network Topology

## Slide 10: Point to Point (PtP) Network Topology
Most basic network topology
Think of it as a simplex QSO between two stations
Can simply link two laptops, a laptop and an IP camera, or even two complex networks
Uses high-gain Yagi or dish antennas

## Slide 11: Point to Multi Point (PtMP) Network Topology

## Slide 12: Point to Multi Point (PtMP) Network Topology
Think of it as a repeater – allows communication between stations unable to reach each other directly
Hub site is potential single point of failure – if it fails, the whole network goes down
Uses omnidirectional or sector antennas

## Slide 13: Mesh Network Topology

## Slide 14: Mesh Network Topology
Very common HSMM topology
Think of it as a wide area simplex net – some stations can relay messages between others that can’t hear each other directly
Resilient – if one station fails, traffic can be routed through others

## Slide 15: Hybrid Network Topology

## Slide 16: Hybrid Network Topology
Large networks will likely be a mix of PtP, PtMP, and Mesh topologies
Separate local networks may be connected over wide area by PtP links, possibly on another band

## Slide 17: HSMM Networking Projects
Broadband-Hamnet, formerly HSMM-MESH
  www.Broadband-Hamnet.org
AREDN (Amateur Radio Emergency Data Network)
  www.AREDN.org
HamWAN
  www.HamWAN.org

## Slide 18: Broadband-Hamnet (BBHN)
Self-discovering, self-configuring mesh network
Replaces stock access point firmware
Supports Linksys and Ubiquiti hardware (see http://broadband-hamnet.org/which-hardware-to-use.htm for supported models)
Little or no networking knowledge required to set up a simple network

## Slide 19: AREDN
Self-discovering, self-configuring mesh network
Replaces stock access point firmware
Supports Ubiquiti and TP-Link hardware (see www.aredn.org/content/supported-platform-matrix for supported models)
Offshoot of BBHN, more feature-rich
Supports 802.11n – higher data rates
Little or no networking knowledge required to set up a simple network

## Slide 20: HamWAN
Planned, engineered network – not automatically discovered/configured like BBHN and AREDN
Standardized on Mikrotik hardware
Setup requires strong data networking and RF engineering skills
Potentially a faster network than BBHN, AREDN
Mix of PtP and PtMP topologies

## Slide 21: BBHN and AREDN Hardware
Linksys
  WRT54G, WRT54GL (only some hardware versions)
Ubiquiti
  Most models in the airMAX M product line
TP-Link
  CPE210, CPE510

## Slide 22: Linksys Hardware

## Slide 23: Linksys Hardware
Pro
  Inexpensive
  Built-in 5-port switch
  Easy way to get your feet wet with Broadband-Hamnet
Con
  Low transmit power (<85mW)
  Low-gain (5dBi) stock omni antennas
  Only available for 2.4GHz band
  Not weatherproof
  Supported models no longer in production

## Slide 24: Ubiquiti Hardware

## Slide 25: Ubiquiti Hardware
Pro
  Higher transmit power (up to 630mW on some models)
  Higher gain stock antennas (7.5dBi – 22.5dBi)
  Models available for 900MHz, 2.4GHz, 3.4GHz, and 5.8GHz bands
  All models fully weatherproof
  MIMO support – higher data rates
  Power over Ethernet (PoE) capability
Con
  No built-in switch
  More expensive for getting started

## Slide 26: What is Multnomah County ARES doing with HSMM?
Evaluating suitability for rapidly field deployable data links, primarily for image transfer and video
Focusing on Ubiquiti radios and AREDN firmware
Currently in learning and experimentation phase

## Slide 27: What have we done so far?
2015 DRT - live video feed from checkpoint
to comms trailer over a 1650’ 900MHz link

## Slide 28: What have we done so far?
Field Test – 3 mile link on 900MHz, 2.4GHz,
and 5.8GHz from Council Crest to parking garage

## Slide 29: What have we done so far?
SeaPac 2016 – Video feed from camera on
roof of hotel across the river from MCARES trailer

## Slide 30: Resources
Wireless Networking in the Developing World (not specific to HSMM but an excellent primer on wireless networking): http://WNDW.net/
AREDN: http://www.AREDN.org
Broadband-Hamnet: http://www.Broadband-Hamnet.org
HamWAN: http://www.HamWAN.org
Washington County ARES: http://WashCoARES.org/?page_id=1227
Santa Clara County ARES: http://www.SCC-ARES-RACES.org/mesh/

## Slide 31: Demonstration

## Slide 32: Questions?